ISADesign:GeneralDesign:C

---
RTS
val3
val2
val1
Stack
CPU
Memory

---
val3
val2
val1

---
result
val1

---
result
ldr/
str
val1

---
result
ldr/
str
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Model Stack ISA:
push [constant]
Push [constant] onto stack.
fetch
Replace address at TOS with value
at that address.
put
TOS is a value; next element is an
address. Pop both and put value
add, sub, mult, div.
Replace top two elements with result of the indicated operation. TOS is second operand.
goto
Pop TOS and jump to that location
goneg
TOS is a test value; next element is
a jump location. Pop both and jump if test value is negative.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
result
val1
Stack Machine:
  Small, fast instructions
  But, more instructions needed

---
Replace top two elements with result of the indicated operation. TOS is second operand.
10000
x
42
a
b
10
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
10004
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
10008
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
32
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.

---
Replace top two elements with result of the indicated operation. TOS is second operand.
32
x
1 push =x @ Stack is =x
2 push =a @ Stack is =a, =x
3 fetch @ Stack is a, =x
4 push =b @ Stack is =b, a, =x
5 fetch @ Stack is b, a, =x
6 sub @ Stack is a-b, =x
7 put @ Stack is empty; x now holds a-b.
 What would be the code for y = a - b*c? Set up initial data so a=42, b=10 and c=3

---
Replace top two elements with result of the indicated operation. TOS is second operand.
y
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c
c
3
 What would be the code for y = a - b*c? Set up initial data so a=42, b=10 and c=3

---
Replace top two elements with result of the indicated operation. TOS is second operand.
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
10004
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
10008
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
10012
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
30
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
push =y
push =a
push =b
push =c
fetch @ Stack is now c, b, a, =y
mult @ Stack is b*c, a, =y
sub @ Stack is a - b*c, =y
put @ Stack is empty; y now holds a - b*c

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
x = e - (a+b)*(c+123) - (42-d)

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
x = e - (a+b)*(c+123) - (42-d)
push =x @ Stack is =x, which we'll need at th end.
push =e @ Stack is =e, =x
fetch @ Stack is e, =x
push =a @ Stack is =a, e, =x
fetch @ Stack is a, e, =x
push =b @ Stack is =b, a, e, =x
fetch @ Stack is b, a, e, =x, ready for some math
add @ Stack is a+b, e, =x
push =c @ Stack is =c, a+b, e, =x
fetch @ Stack is c, a+b, e, =x
push 123 @ Stack is 123, c, a+b, e, =x
add @ Stack is c+123, a+b, e, =x
mult @ Stack is (a+b)*(c+123), e, =x
push 42 @ Stack is 42, (a+b)*(c+123), e, =x
push =d @ Stack is =d, 42, (a+b)*(c+123), e, =x
fetch @ Stack is d, 42, (a+b)*(c+123), e, =x
sub @ Stack is 42-d, (a+b)*(c+123), e, =x
sub @ Stack is (a+b)*(c+123) - (42-d), e, =x
sub @ Stack is e - (a+b)*(c+123) - (42-d), =x
put @ Stack is empty. X contains computed value

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
Infix Postfix
a+b ab+
a + b*c a(bc*)+
a - b - c a b-c-
a - (b-c) abc-- or a(bc-)-
a - (2 - c*d) a2cd*--
a - (b-c)*2 abc-2*-
(a - b - c)*2 ab-c-2*
(a - (b-c))*2 abc--2*

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
Infix Postfix
a+b ab+
a + b*c a(bc*)+
a - b - c a b-c-
a - (b-c) abc-- or a(bc-)-
a - (2 - c*d) a2cd*--
a - (b-c)*2 abc-2*-
(a - b - c)*2 ab-c-2*
(a - (b-c))*2 abc--2*
Infix => Postfix
a*b - 42*d - e
a*b - (42*d - e)
a*(b - 42*(d - e))
a*(b - 42)*d - e

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
Infix Postfix
a+b ab+
a + b*c a(bc*)+
a - b - c a b-c-
a - (b-c) abc-- or a(bc-)-
a - (2 - c*d) a2cd*--
a - (b-c)*2 abc-2*-
(a - b - c)*2 ab-c-2*
(a - (b-c))*2 abc--2*
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
Infix Postfix
a+b ab+
a + b*c a(bc*)+
a - b - c a b-c-
a - (b-c) abc-- or a(bc-)-
a - (2 - c*d) a2cd*--
a - (b-c)*2 abc-2*-
(a - b - c)*2 ab-c-2*
(a - (b-c))*2 abc--2*
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -
Postfix => Infix
a b c d - * -
a b - c * d -
a b c - * d -
e a b + c 123 + * - 42 d - -

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
Infix Postfix
a+b ab+
a + b*c a(bc*)+
a - b - c a b-c-
a - (b-c) abc-- or a(bc-)-
a - (2 - c*d) a2cd*--
a - (b-c)*2 abc-2*-
(a - b - c)*2 ab-c-2*
(a - (b-c))*2 abc--2*
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -
Postfix => Infix
a b c d - * - => a - b*(c-d)
a b - c * d - => (a - b) * c - d
a b c - * d - => a*(b-c) - d
e a b + c 123 + * - 42 d - - => e - (a+b)*(c+123) - (42-d)

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
loopTop:
push =afterLoop
push 42
push =i
fetch @ Stack: i, 42, =afterLoop
sub @ Stack: 42 - i, =afterLoop
goneg @ Goto afterLoop if 42 - i < 0
push =i @ Location for future "put"
push =i @ Stack: =i, =i
fetch i @ Stack: i, =i
push 1 @ Stack: 1, i, =i
add @ Stack: i+1, =i
put @ i is now incremented.
push =loopTop @ Stack: =loopTop
goto @ Stack: empty Back to loopTop
afterLoop:
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -
Postfix => Infix
a b c d - * - => a - b*(c-d)
a b - c * d - => (a - b) * c - d
a b c - * d - => a*(b-c) - d
e a b + c 123 + * - 42 d - - => e - (a+b)*(c+123) - (42-d)

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
loopTop:
push =afterLoop
push =i
push 42 @ Stack: 42, i =afterLoop
sub @ Stack: i - 42, =afterLoop
goneg @ Goto afterLoop if i - 42 < 0
push =i @ Location for future "put"
push =i @ Stack: =i, =i
fetch i @ Stack: i, =i
push 1 @ Stack: 1, i, =i
add @ Stack: i+1, =i
put @ i is now incremented.
push =loopTop @ Stack: =loopTop
goto @ Stack: empty Back to loopTop
afterLoop:
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -
Postfix => Infix
a b c d - * - => a - b*(c-d)
a b - c * d - => (a - b) * c - d
a b c - * d - => a*(b-c) - d
e a b + c 123 + * - 42 d - - => e - (a+b)*(c+123) - (42-d)

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
loopTop:
push =afterLoop
push =i
push 42 @ Stack: 42, i =afterLoop
sub @ Stack: i - 42, =afterLoop
goneg @ Goto afterLoop if i - 42 < 0
push =i @ Location for future "put"
push =i @ Stack: =i, =i
fetch i @ Stack: i, =i
push 1 @ Stack: 1, i, =i
add @ Stack: i+1, =i
put @ i is now incremented.
push =loopTop @ Stack: =loopTop
goto @ Stack: empty Back to loopTop
afterLoop:
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -
a < b a < b
a > b b < a
a <= b !(a > b)
a >= b
a != b a < b || b < a
a == b
Postfix => Infix
a b c d - * - => a - b*(c-d)
a b - c * d - => (a - b) * c - d
a b c - * d - => a*(b-c) - d
e a b + c 123 + * - 42 d - - => e - (a+b)*(c+123) - (42-d)

---
Replace top two elements with result of the indicated operation. TOS is second operand.
12
loopTop:
push =afterLoop
push =i
push 42 @ Stack: 42, i =afterLoop
sub @ Stack: i - 42, =afterLoop
goneg @ Goto afterLoop if i - 42 < 0
push =i @ Location for future "put"
push =i @ Stack: =i, =i
fetch i @ Stack: i, =i
push 1 @ Stack: 1, i, =i
add @ Stack: i+1, =i
put @ i is now incremented.
push =loopTop @ Stack: =loopTop
goto @ Stack: empty Back to loopTop
afterLoop:
Infix => Postfix
a*b - 42*d - e => a b * 42 d * - e -
a*b - (42*d - e) => a b * 42 d * e - -
a*(b - 42*(d - e)) => a b 42 d e - * - *
a*(b - 42)*d - e => a b 42 - * d * e -
a < b a < b
a > b b < a
a <= b !(a > b)
a >= b !(b > a)
a != b a < b || b < a
a == b !(a < b || b < a)
Postfix => Infix
a b c d - * - => a - b*(c-d)
a b - c * d - => (a - b) * c - d
a b c - * d - => a*(b-c) - d
e a b + c 123 + * - 42 d - - => e - (a+b)*(c+123) - (42-d)